## Creating an ECU configuration project:

- No target board can be selected since RPi is not supported in ArcticStudio 4.1 (should we download version 6?)
- We skip imorting application model from SWCD in this example (no SW-C's here, we call drivers directly).
- After all the steps. Go to System Services Configuration. In BSWEditor:
  - EcuM – not in the tools since RPi is not there
  - Only Os can be configured
    - Add Os
    - Double-click Os
    - Right-click Os
    - Create Os-alarms, Os-application, Os-counter, Os-event, Os-task
      - OsOS:
        - Change Arc Os Tick Frequency to 1000 (means 1 tick per 1000 microseconds or 1/ms, however this is a bit fake, we have our own solution (since MCU cannot be configured for RPi))
      - Os-counter:
        - delete max allowed value;
        - Os-counter type -> OS_TICK
      - Os-event:
        - Change event shortName
      - Os-task:
        - Change task shortName
        - Select Os Task Event Ref and choose the above event (this means that the event will trigger the task)
        - Choose priority (e.g. lowest (low nr, e.g. 2 (since we already have an idle task)))
        - Right-click and choose “Create OsTaskAutostart” (this triggers the task the first time, at creation)
        - Create another task, StartupTask (priority: highest (in this example: 3)). Create OsTaskAutoStart also for this task.
      - Os-alarm:
        - Change alarm shortName
        - Set Os Alarm Counter Ref to Os-counter (then the alarm will be triggered by the counter, i.e. by OS_TICK)
        - Right-click OsAlarmAction and choose Create OsAlarmSetEvent.
        - Choose OsAlarm Set Event Ref to the Os-event we have created.
        - Choose OsAlarm Set Event Task Ref to the Os-task we have created. (Do we really need both of these references???)
        - Right-click on the Alarm and
          - Create OsAlarmAutostart
          - Set Alarm time (time to first trigger)
          - Set Alarm Autostart Type to ABSOLUTE
          - Set Cycle time (inter-alarm time period)
      - Os-application:
        - Change name
        - Select and choose all Os-alarm, counter and task Refs (if more than one, click on + besides an already existing Ref to add the second one, etc). In our example, add StartUp task ref.
  - In the upper-right corner, click on the second button (“Generate Os”). Os_cfg.c/h-files are created
- Copy from an existing project the following files (from config/): Det, Dio, Dma, EcuM, Mcu, Port, (Pwm) _Cfg.h/c (trademark: Shuzhou during his MSc-thesis). Can be reused for all our projects. (This shouldn't be necessary if these files were in core/RPi/config. Move it there when everything works.)
- In the makefile: add “build-bin-y = kernel.img”
- In build_config.mk: add the modules that we use, for example: “MOD_USE = DET DIO DMA ECUM MCU KERNEL PORT PWM”
- Add the main file to the root of the project:
  - Create new c-file.
  - Add/copy implementations of the defined tasks, e.g.
    - void OsIdle(void) {}
    - void StartupTask(void) {}
    - void DriverTesterTask(void) {}
- Set up build properties
  - Right-click the project -> Properties -> C/C++ Build -> Environment and edit the BOARDDIR to “Raspberry_Pi” (this is the name of our board folder in core/).
- Right-click and build the project!

Minicom setup on Linux:
- sudo apt-get install minicom
- sudo minicom
- Ctrl+A, Z -> cOnfigure Minicom -> Serial port setup ->
  - A (Serial Device) -> /dev/ttyUSB0
  - E (Bps/Par/Bits) -> 115200 8N1
  - F (Hardware Flow Control) -> No (very important!)
- Save setup as “pi”
- Ctrl+A, X
- Next time just type sudo minicom pi
- To transfer files Ctrl+A, S; Then choose xmodem and kernel.bin (kernel.img for the bootloader must already be on the SD-card)
## How to create a SW-C
See http://download.arccore.com/asr4/user-doc/UD460x/Working-with-SWCs_10191241.html
## How to add a port to a SW-C
Open ArcticStudio, using the following workspace: C:\Users\sse\ArcticStudio3\workspace\fresta_v1
Choose tab “Autosar Navigator” (this one is for the .arxml-projects, while the Project tab is for the C-code).
If necessary, define variable types in Types.swcd, for example:
int impl UInt8 extends uint8
If necessary, create a new interface for the new port (double-click on the Interfaces.swcd), to define what kind of data this port will support. For example:
interface senderReceiver SRInterface3 {
data UInt32 dataInt32
}
The list of ports is defined in Components.swcd. Add a new port definition in an appropriate SW-C, for example:
receiver PortName requires SRInterface3
If necessary, create a new Runnable (under internalBehavior in Components.swcd).
For each provided port, add dataWriteAccess definition.
For each required port, add dataReadAccess and dataReceivedEvent definitions.
Now, connect the port(s). Let's go to Extract.swcd...
External connection: Add a @signalMappings-tag for each external (to ECU) signal. This is a mapping between port name (as a part of SWC-instance) and an incoming PDU-signal (pre-defined in another place).
Internal connection: Just use the connect keyword (write to read)
Finally... Go to Merged Model (don't double-click this time). Select everything, right-click and EXport to Autosar xml -> Select c-project and go!
Go to Project Explorer. Right-click on VCUEcuConfiguration.arxml. Open With BSW Editor for Autosar 4. Select (to the right) the new ecuExtract.
Right-click on VCUEcuConfiguration.arxml. Open With RTEitor for Autosar 4. Remove all old entities (those invalid ones with the question marks).
Define new events to the Os configuration (in BSW editor) and add them to appropriate tasks.
Go back to RTE editor, right-click on every entity and instantiate it.
Map between Components-events and Os-events. Right-click on each entitie's event, map it to a task and select an Os event (to the right).. Also, specify a number for the Position (in the generated code).
Finally, when (if) everything works (seems buggy though in the tools), generate code!!!
## How to add Types
For every new project, we need to define (or import from existing projects) which variable types we're going to use, for example:
int impl UInt8 extends uint8
Sometimes (or quite often), we get an error “Unresolved blah-blah”. Then click in the following fields (uint8) in the SwDataDefProps (see the figure below).